## Slide 1
METLEN-SCALE BESS SIMULATOR
From scarce telemetry to feasible battery dispatch
A submission-ready Greek DAM demo: public data in, constraint-aware dispatch out, with a storage-aware regime-shift caveat.
330 MW
790 MWh
15-minute DAM
2.39h
METLEN nameplate duration
10-90%
SoC modeling convention
85% / 90%
RTE base and optimistic sensitivity
Team walkthrough deck | ETW Hackathon

## Slide 2
GREEK PROBLEM
The hard part is not scheduling a battery. It is scheduling without Greek battery history.
Standalone BESS is entering the Greek market, but mature telemetry and observed bidding behavior are not available yet.
No mature telemetry
Greek standalone BESS behavior is not a stable training label yet.
Public signals
HEnEx DAM, IPTO forecasts, and weather become the reproducible data backbone.
Hard constraints
The schedule must respect SoC, power, efficiency, terminal SoC, cycles, and degradation.
Submission stance: scenario analysis, not a claim of exact post-launch Greek prices.

## Slide 3
BATTERY OPERATIONS
The demo mirrors the operator loop, then marks the layers not yet modeled.
1
Pre-market planning
Build price, load, RES, weather, and constraint view.
2
DAM optimization
Choose charge, discharge, or idle across 96 quarter-hours.
3
Intraday update
Future layer for forecast errors and imbalance risk.
4
Services headroom
Future layer for reserve and balancing value stacking.
5
Settlement review
Revenue, degradation, throughput, cycles, and spread captured.
Implemented now: pre-market data frame, DAM optimization, and settlement review. Next: intraday, balancing, ancillary services, thermal derating.

## Slide 4
DATA STACK
Everything in the demo is traceable to public inputs or explicit assumptions.
HEnEx
15-minute DAM MCP prices and future aggregated curves
IPTO
load and RES forecasts for market context
Open-Meteo
radiation, cloud, wind, and temperature features
Chart: Live-safe vs diagnostic feature split
| Live-safe | Diagnostic | Fallback
Feature families | 6 | 4 | 1
Leakage rule: post-clearing DAM prices, accepted volumes, and curve slopes are diagnostics unless timestamp checks prove they were available before the decision.

## Slide 5
SIMULATOR METHODOLOGY
MILP first; market-impact scenario second.
The core optimizer remains price-taker and constraint-pure. The regime-shift layer is deliberately labeled as counterfactual sensitivity.
Decision variables
charge MW, discharge MW, SoC, and binary mode guard for each 15-minute interval
Constraints
power, energy, SoC band, terminal SoC, efficiency, degradation, cycle budget, no simultaneous charge/discharge
Objective
maximize DAM arbitrage net of throughput/degradation cost under the selected price signal
Regime shift
charge lifts trough prices, discharge suppresses peaks, larger fleets compress spreads

## Slide 6
DEMO READOUT
What the judges should see in two minutes.
Feasible dispatch
Every schedule obeys the battery and terminal-SoC constraints.
Sensitivity surface
Efficiency, cycles, and degradation are assumptions, not fixed facts.
Revenue haircut
Storage-aware scenarios show why pre-battery spreads may overstate value.
Chart: Illustrative value framing
| Price-taker | Low impact | Medium impact | High impact
Relative net value | 100 | 93 | 86 | 76
Evidence framing: Italy/Spain are closer market analogues; CAISO/NREL inform storage valuation; AEMO is operational evidence that renewables plus batteries can put downward pressure on wholesale prices.